DISPOSABLE DIAPERS AND ABSORBENTS MACHINE

USER’S GUIDE

__________________________

# HANDLING THE MACHINE

Greetings

Congratulations on the purchase of  your Unique  Affordable Diaper/Nappy Machine. The Machine is designed to work constantly  without affecting the mechanism/electrical components.

____________________________________

# PROCEDURES TO BEGIN THE WORK

- Switch the Machine on and turn thermostat to require temperature, once temperature is reached the pilot ligth will switch on/off regulating the temperature.

- Turn thermostat up to a maximum of 150 degrees or to the temperature that gives the glue a “ Honey Like” texture (+/- 120 minutes before operating).

- To put the Polyethylene roll in place lift the lid of the Machine, which is near the mechanism, using the metal Rod as well as the wooden disk. (Put one [1] wooden disk in each Poliethylene cone ends.)

Use the black rubber disk to centerise the roll of polyethylene.

Once the polyethylene is in place lift up the rubber roll from the rod with the plastic disc/ fibre wheels and put polyethylene between the fibre washer rod and rubber roll. Then pull the polyethylene all the way to the back of  the machine and squeeze between pressure rollers.

______________________________________________________

GETTING TO KNOW YOUR MACHINE – SEE PICTURE PAGE A

Instructions for assembly and for manufacturing nappies and absorvents.

- Rubber Roll.

- Automatic Elastic Placer.

- Feet (4 Pieces) plus 2 Connecting Bars to stabilize the feet.

- Columns for supporting the Non – Woven Roll.

- Lid for Pulley Protection.

- Linking Plug on the  Motor and foot Pedal to operate the Machine.

- Removable Lid.

- Roll of Non-Woven supported by rod, which hás 2 wheels made of  wood and 4 rubber Disks to centralize the roll.

- Settings to regulate the Pressure of the Non-Woven and Polyethylene, when they come together to form the Nappy.

- The inside of the Machine, removing the removable lid. (7) You will find 1 aluminium rod for supporting the Roll.

- Operatio Pedal.

- Pressure Rolls made of rubber.

- Heating Element.

- Heating Element Plug.

- Main Switch (on/off).

- Thermostat – Control Knob

- Pilot Light indicates if the Thermostat is working.

- Fibre Disk rod to control glue lines on the Polyethylene (regulates the glue onto the Polyethylene).

- Thermostat Rod – transmits the temperature of the glue to the thermostat placed deep into the little tank of glue throught the hole indicated in the picture. Doublé check Cooper rod (end) is totally submerged into glue tray.

Note: All Legs have 3 holes, and to assembly these line up with the machine holes.

## NON-WOVEN

Install same as Polyethylene.

Once in place squeeze through pressure rolls same as Polyethylene.

NOTE: Non-woven, neathy unroll, place one weight of more or less 150 grams above the roll, held with a string or to create tié tags/ toughness finish etc. Note the width of Non Woven is wider than the Polyethylene width.

## ASSEMBLY

Pre-cut Padding with 100% more Super Absorbent Gel

Newborn                                      10 cm Width x 25 cm Length.

Small                                            10 cm Width x 28 cm Length.

Médium Nappies                          10 cm Width x 30 cm Length.

Large Nappies                              10 cm Width x 35 cm Length.

X-Large Nappies                          10 cm Width x 40 cm Length.

Geriatric Liners

Place Padding on the Polyethylene – remember to only place padding as shown – the glue on the elastic are your indicator.

_____________________

### MECHANISM SET-UP

- Place the small rubber roll in the position 1 suspended, as it is shown in the diagram B.

- Take the elastic tip from one of the elastic rolls without splitting, and pass between the upper sand paper roll and the compreesor roll. Separate the elastic into 3 strips and pass each one through the existing holes in the plastic ruler (Leaving the inside hole on each side of the plastic ruler open.) Now put them around the bottom sand paper roll and take them up as indicated by the arrows. Go by the first rod of the glue through the channels of the second rod, under the small rubber and let them hanging with the lenght of about 15 cm. Repeat the operation with the elastic of the other side.

- Take the polyethylene tip, pass under the rubber roll above (involving the small cylinder) as it is shown in the diagram and pull across the whole lenght of the machine, till it passes between two compressor rolls.

- Take the elastic and stretch them in more or less 3 times its original extension, hold them with the tags.

- The elastic will receive glue when touching the cylinder, at various intervals according to the size of the nappy that you will produce. The spaces that have no glue are the empty space between one nappy and the other one, and will be cut afterwards.

- To start the production of nappies or absorbents, it is necessary to put the rubber rod (1), leaned on the rod of the fiber washer.

- During the time that the machine is not producing, make sure elastic are not touching the cylinders for glue collection of  the elastic (this lifts the elastic away from the glue). The rubber roll should be in a locked up position. (In suspension).

SEPARATION OF THE NAPPIES AND OPTIONAL CUTTING OF THE LEGS

Separate the nappies by cutting on the straight blade of the guilhotine and use your angle blade (optional) to cut legs.

PLACING DECORATIVE/ TAG TAPE

Cut the Decorating tape 25 cm in lenght, placing it at one end of  the nappy. Tie Tag – Place at the  opposite end of the nappy and fasten one tie tag on to each side of the opposite end of the decorative tape. Stick the transparent part of the tie tag onto the outside of the nappy (on to the non-woven). Note the height of the Decorative tape in relation to where the tie tag are being stuck.

Repeat the oparation to the other side, fold the nappy that is ready and pack in the desired amount, sealing the package with the bag sealer.

ASSEMBLY OF GERIATRIC LINERS

Take Pre-Padding and place in the center of the Polyethylene roll. Leave one hand space between each pad.

It is not common to use elastics in the Geriatric Nappies. It is possible to manufature pads for after childbirth and Adult Absorbents.

_____________

THE NAPPIES

The should be  put in the machine with 7 cm of distance between one another (noting the lenghts of glue on the elastics). Then after having passed through the machine the units must be cut. Cut the legs; place the decorative tape in the frontal part and the tie tag on the opposite end.

________________________________

MAINTENANCE / INSTRUCTIONS

- HYGIENE AND CLEANING

It is very important to keep the work place clean, protecting the equipment, the raw material and the finished products.

The raw material is delivered pre-sterilized, make sure hands are clean when operating.

As the air is naturally polluted. It is importan to  wrap the finished products as soon as they leave the machine for the finishing.

- PACKING

The nappies and absorbents should be wrapped in plastic bags, and they can be closed with our sealing machine. The opaque and milky plastic is better than the transparent ones.

We suggest the following quantities for wrapping:

Baby Nappies:                     6/1224/36 or 48 units

Geriatric Liners:                 10 or 20 units.

Sanitary Pads:                     10/20 or 30 units.

* For good exposure of brand – create your own packaging

The printed bags show a better presentation.

NOTE: It is important that the machine is always leveled and clean.

# Text boxes

#### TIPS

- From  time to time when glue is hot while in production use something to  rotate/mix hot glue in the gluctray to prevent cold spots.

- Glue lines must be thin to avoid excess usage of glue.